## Slide 1
Real Time Image Process
Ryunosuke Murakami
murakar@rose-hulman.edu
Kuangyi Lu
luk@rose-hulman.edu
Rose- Hulman Institute of Technology
TMDS Video Format
Image Process Algorithms
Image overwrite function was implemented, which display image data stored in BRAM
Zynq PS write image data into BRAM via SDK
AXI 4 interface is used to connect Zynq PS and BRAM via BRAM controller module
PS Function
Manage current position of output
  count Horizontal address with pixel clock from TMDS
  count Verical address with active of Horizontal Synchronization pulse
  Current position will be reser with Vertical Synchronization pulse
Image data is stored from SDK
  can change contents without synthesizing
Connected with both PS and PL module
  PS connection: via AXI interface
  PL connection: Image Process
BRAM
Line Buffer
Overview of System
TMDS Timing Manager
ECE Department
ECE530
Software and Hardware Co-Design with Zybo
Instructor: Jianjian Song
Store pixel data into memory cell
  memory cell size 1280
4 lines of memory module is used
  3 lines for img process algorithm
  1 line for storing ongoind pixel
Each line buffer rotates when its memory cell is full stored.
TMDS image processing system was designed with verilog HDL with
  4 line line Buffer
  Image Processing algorithm
  TMDS Timing Manager
PL Design
Applied Algorithms
  Gray Scale:
    Color to balck and white
  Neg Pos Inv:
    Invert luminance
  Gausian filter:
    smoothing effect (σ=1.3)
  Emboss filter:
    emphasize emboss outline
  Laplacian filter:
    Edge detection
  Sobel filter:
    Edge detection + emboss
Data output is controlled with video active signal
Hsync indicate line end
Vsync indicate frame end
Pixel wise and Window wise algorithms were implemented
3x3 filter (Convolution operation) was applied